## Slide 1
Satellites for Meteorology and Weather Forecasting
Ross Bannister
High Resolution Atmospheric Assimilation Group,
NERC National Centre for Earth Observation, University of Reading, UK, r.n.bannister@reading.ac.uk
Observations
Meteorological model
Weather forecasts
data
assimilation
(‘initial conditions’)

## Slide 2: How do satellites help in understanding and forecasting weather events?
There is a huge demand for up-to-date knowledge about the Earth system
Issues with use of satellite data for numerical weather prediction (NWP)
1 | Model forecasts stray from reality over time (chaotic destruction of knowledge). The ‘butterfly effect’.
2 | The world is a very large place! Volume of atmosphere: 5 billion km3.
1 | Satellites don’t measure directly meteorological quantities (winds / temperature / humidity / etc). These have to be inferred for use with models: data assimilation.
2 | Qualitative information from satellites (‘satellite pictures’) help us see the evolving atmosphere, but doesn’t satisfy this demand.
3 | Satellite data need to be treated quantitatively to be useful for numerical weather forecasting.

## Slide 3: Types of weather measurements
 |  | Coverage |  |  |  | Resolution | 
Instrument | Quantities | Spatial |  | Temporal |  | Horiz. | Vert.
In-situ instruments |  |  |  |  |  |  | 
Radiosondes | u, v, T, p, q, (O3) | Cont. N.H., t-sphere | 6 hourly |  |  | point | point
Surface stations | u, v, T, p, q | Continental surface | 6 hourly |  |  | point | n/a
Aircraft | u, v, T, p, q | Flight paths, airports | In flight |  |  | point | point
Drifting buoys | u, v, T, p | Drift paths, sea level | hourly |  |  | point | n/a
Remote sensing instruments |  |  |  |  |  |  | 
Geostationary satellites | Rad: MW, IR, Vis | Global |  | 15-30 mins | > 10 km |  | many kms
Polar orbit satellites (nadir) | Rad: MW, IR, Vis | Global |  | Continuous | 100s m |  | many kms
Polar orbit satellites (limb) | Rad: MW, IR, Vis | Global |  | Continuous | 100s km |  | 1-2 km
Scatterometer | Radar backscatter | Oceans |  | Continuous | 50 km |  | n/a
Radio occultation | GPS phase shifts | Global |  | ~ hourly | 150–300 km |  | 1 km
Ground-based radar | Radar reflectivity / Dopler shift | N.Am., Eu., Australia. 200km from antenna |  | 10 mins | ~ 1° |  | 
not comprehensive!
'Rad'=radiances, 'MW'=microwave, 'IR'=infrared, 'Vis'=visible
In operational global weather forecasting there are ~108 observations assimilated per cycle

## Slide 4: Coverage maps for NWP
Courtesy Met Office

## Slide 5: Contents
PART A | A history of satellites for weather forecasting / Earth observation
PART B | What does a satellite ‘see’?
PART C | Types of satellite orbit / viewing geometry / instrument
PART D | Example imagery
PART E | Deriving useful information from satellite measurements

## Slide 6: A history of satellites for weather forecasting
Feb 1959 – Vanguard 2
Aug 1959 – Explorer 6
Apr 1960 – TIROS 1
1969 – Nimbus 3
1966 – ATS (geostationary)
1974 – SMS (geostationary)
1978 – MeteoSat (geostationary)
2004 – MeteoSat SG (geostationary)
2006 - MetOp
First picture of Earth from TIROS-1
not comprehensive!

## Slide 7: Sequences of satellite pictures (visible)
www.sat.dundee.ac.uk
SEVIRI channel 1, 0.56 – 0.71 μm
Courtesy NERC Satellite Receiving Station, University of Dundee

## Slide 8: Information from satellite measurements over other parts of the EM spectrum
Wavelength 10-6 m (µm)
‘radiance’ measured by satellite
Thermal emission
from body at 300K
9.7 µm - information on temperature at ~13 km
12.0 µm - information on temperature near the surface to ~3 km
7.3 µm - information on temperature at ~3 to ~8 km
Max Planck

## Slide 9: Sequences of satellite images (visible + infrared)
www.sat.dundee.ac.uk
SEVIRI channel 1, 0.56 – 0.71 μm
SEVIRI channel 10, 11 –13 μm
Courtesy NERC Satellite Receiving Station, University of Dundee

## Slide 10: Sequences of satellite images (visible + infrared + water vapour)
www.sat.dundee.ac.uk
SEVIRI channel 1, 0.56 – 0.71 μm
SEVIRI channel 10, 11 –13 μm
SEVIRI channel 6, 6.85 –7.85 μm
Courtesy NERC Satellite Receiving Station, University of Dundee

## Slide 11: Flow regimes

## Slide 12: Geostrophic balance
L
Gaspard-Gustave de Coriolis

## Slide 13: Orbit configurations
Polar orbit
600 - 800 km above sea level typically.
Near-global coverage over time.
Non-continuous sampling of a given location.
Often used for sounders (e.g. on board EnviSat, EOS Aura, etc).
Geostationary orbit
• 35 786 km above sea level, latitude 0.0°.
• View 1/4 of Earth's surface (60S-60N).
• Continuous sampling of a given location.
• Often used for imagers (e.g. on board MeteoSat, etc).
• Horiz. resolution degrades poleward.
12

## Slide 14: Viewing geometries
Limb
• Good vertical resolution possible (~1km).
• Poor horizontal resolution.
• Used mainly in research.
Nadir
• Good horizontal resolution possible.
• Poor vertical resolution (several km).
• Used mainly in operational weather forecasting.

## Slide 15: Satellite ‘imagers’ vs ‘sounders’
Imager:
An instrument that measures a signal with spatial resolution.
On board geostationary and polar orbiting satellites.
Nadir viewing only.
Sounder:
An instrument that measures a signal with spectral resolution.
On board mainly polar orbiting satellites.
Nadir or limb viewing.
Can be processed to give quasi-height resolved retrievals of T, q, O3, etc. (used heavily for numerical weather prediction).

## Slide 16: Selection of instruments
not comprehensive!
List of more acronyms at www.met.rdg.ac.uk/~ross/DARC/Acronyms.html

## Slide 17: Other types of satellite instrument
Scatterometer Radio occultation

## Slide 18: Forecast accuracy
Take the average accuracy of a 1-day forecast in 1980.
How long does a forecast have to be (subsequently) to achieve this accuracy?
Courtesy Met Office
Courtesy ECMWF
How close is forecast to latest analysis?
Northern hemisphere
Southern hemisphere

## Slide 19: Example imagery – polar lows
Courtesy NERC Satellite Receiving Station, University of Dundee
06/04/2007, MODIS 30/03/2013, MODIS

## Slide 20: Example imagery – frontal systems
Courtesy NERC Satellite Receiving Station, University of Dundee
31/01/2008, MODIS 08/12/2011, MODIS 22/03/13, AVHRR

## Slide 21: Example imagery - thunderstorms
Courtesy NERC Satellite Receiving Station, University of Dundee
30/10/2008, AVHRR 24/04/2008, MODIS

## Slide 22: Example imagery - hurricanes
Courtesy NERC Satellite Receiving Station, University of Dundee
29/08/2005, GOES-E 29/10/2012, GOES-E

## Slide 23: Example imagery - anticyclones
Courtesy NERC Satellite Receiving Station, University of Dundee
09/12/2001, MODIS 21/09/2006, MODIS

## Slide 24: Example imagery – other features of interest
Courtesy NERC Satellite Receiving Station, University of Dundee
03/04/2011, MODIS 07/05/2010, MODIS 20/03/2009, AVHRR
27/03/13, AVHRR

## Slide 25: Deriving useful information from satellite data
Measured brightness
temperature (K)
wavenumber (cm-1)
Simulated brightness
temperature (K)
wavenumber (cm-1)
compare simulated with measured spectra
adjust atmospheric profiles for greater agreement
(retrieval / assimilation theory)
simulate spectrum
Estimation of atmospheric state refined with information from measured spectrum
Temperature water vapour O3

## Slide 26
SEVIRI channel 6, 6.85 –7.85 μm
Courtesy NERC Satellite Receiving Station, University of Dundee
Ref: From Sputnik to EnviSat, and beyond: The use of satellite measurements in weather forecasting and research
Brugge & Stuttard, Weather 58 (March 2003), 107-112; Weather 58 (April 2003), 140-143.